## Slide 1: WF on the three “evaluate and, if needed, specify” Items
Nokia, Alcatel-Lucent Shanghai, Samsung, CATT
3GPP TSG RAN WG1 Meeting #85
Nanjing, China 23rd - 27th May 2016
Agenda item: 6.2.3.
R1-165790

## Slide 2: Proposal: UL DMRS enhancement
Specify enhancement on uplink DMRS to support (more than 2) orthogonal DMRS for MU-MIMO with partially overlapping BWs allocation, i.e. IFDMA with OCC2 and/or new DMRS sequence design

## Slide 3: Proposal: advanced CSI
Specify enhancement on CSI reporting based on non-precoded and beamformed CSI-RS to improve eNB precoding. The specified enhancement is to be selected from the following categories:
  Implicit feedback based on linear combination codebook (LCCB) for NP and BF CSI-RS; and/or
  Explicit feedback for NP and BF CSI-RS, including LCCB-based channel/eigenvector quantization and/or channel covariance matrix quantization.
In addition, interference measurement enhancement can be considered

## Slide 4: Proposal: DMRS-based semi-open-loop
Specify enhancement to support DMRS-based semi open-loop transmission with the existing numbers of CSI-RS ports as well as the newly supported number of CSI-RS ports, in the following areas
  CSI reporting scheme with partial PMI feedback, and
  Transmission method with transmit diversity and/or precoder cycling and/or precoder bundling