## Slide 1: Way Forward on Mechanism for MUST operation
MediaTek, China Telecom, CHTTL, CMCC, Huawei, HiSilicon, HTC, III, ITRI,
NTT DOCOMO INC., NTU, Sharp, Sony, ZTE
R1-165799
3GPP TSG-RAN WG1 #85
Nanjing, China, 23rd – 27th May 2016
Agenda item 6.2.4.2

## Slide 2: Proposals for MUST Operation
No new TM for MUST
MUST Case 1 and Case 2 using up to 2Tx is supported in the following TMs
  TM 2/3/4
  FFS TM 8/9/10
MUST Case 3 using up to 8Tx is supported in the following TMs
  TM 4/8/9/10
New DCI for MUST introduced for specific TMs
  FFS on details of new DCI for MUST
RRC signalling used to indicate when UE needs to monitor new DCI for MUST
  MUST-near UE may assume MUST interference presence/absence is consistent among all of its scheduled PRBs for CRS-based TM
  FFS DMRS-based TM