## Slide 1: WF on NR UL MIMO
Intel, NTT DoCoMo, Ericsson
R1-165808
3GPP TSG RAN1 #85
Nanjing, China, May 23 - 27, 2016
Agenda Item: 7.1.6

## Slide 2: Background
In R1-163884, R1-163885 and email discussion [84b-13], number of antenna elements at TRP/UE is agreed:
  @700MHz: up to 64 @TRP and up to 4 @UE
  @4GHz: up to 256 @TRP and up to 8 @UE
  @30GHz: up to 256 @TRP and up to 32 @UE
  @70GHz: up to 1024 @TRP and up to 32 @UE
With larger number of antenna elements @TRP at all NR bands and new UE hybrid antennas @UE, this WF summarizes companies’ views with regard to NR UL MIMO design
In order to fully reap the gain of large number of antennas in NR system, UL MIMO needs to be enhanced compared to LTE UL MIMO

## Slide 3: NR UL MIMO technologies
The following techniques are studied for NR UL MIMO
  Uplink transmission/reception schemes for data channels
    Spatial multiplexing
      Non reciprocity based UL MIMO (e.g. PMI based)
      Reciprocity based UL MIMO
      Multi point spatial multiplexing
        e.g. different layer is received by different TRP
        Note: multiple point may have coordination
      @>6GHz
        UL analog beamforming management
    Spatial diversity
      open loop and semi-open loop UL MIMO
      Uplink antenna / panel switching (UE side)
      Multi point reception
      @>6GHz
        Multi panel spatial diversity
  SRS/DMRS design for UL MIMO
    @>6GHz, other RS, e.g. phase noise compensation RS
  UL power/timing control
  Transmission scheme for UL control channel, e.g. UCI or random access
  Other techniques are not precluded