## Slide 1: WF on Scalable Numerology Symbol Boundary Alignment
Panasonic, InterDigital, Ericsson, Fujitsu, NTT DOCOMO,
update from R1-165583
3GPP TSG RAN WG1 #85 R1-165821
Nanjing, China
23th – 27th May 2016
Agenda item:7.1.4
Document for decision

## Slide 2: Proposal
In case of working assumption of F0=15 kHz, with Fs=15 kHz symbol boundary of normal CP is aligned with LTE.
For scaled numerology Fs = F0*M, in the case where Base numerology contains N symbols per ms and scaled numerology contains N*M symbols per ms
  Each symbol length (including CP) of base numerology (w/ SCS = F0) equals the sum of the corresponding M symbols of scaled numerology (w/ SCS = Fs)
  Each symbol may not necessarily be of the same length (e.g. in LTE numerology, symbol0 is long than symbol 1, 2, … 6)
  Multiple CP durations per each numerology is not precluded:
    For each CP family (NCP or ECP), each symbol length (including CP) of base numerology (w/ SCS = F0) equals the sum of the corresponding M symbols of scaled numerology (w/ SCS = Fs)
Above is not related to synchronization among multiple transmitters like network synchronization, synchronization among UEs, different NR carrier bandwidth and so on.