## Slide 1: WF on DL broadcast enhancement for V2X
Huawei, HiSilicon, Ericsson,..
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23rd – 27th May 2016
Agenda item: 6.2.9.3
R1-165844

## Slide 2: Proposal 1
The LS reply from RAN1 to RAN for LTE/DSRC coexistence includes in principle the points captured in next slides.

## Slide 3: Proposal 2
RAN1 believes that other radio access technologies may efficiently detect LTE-based ITS transmissions on sidelink if necessary action is taken in other SDOs.
The possible solutions identified by RAN1 for high level coexistence approaches (long-term basis) between PC5 transport for V2V services and DSRC/IEEE 802.11p services in the same channel are as follows:
  Geo-location and database
  Transmission of predetermined signal(s) e.g. LTE-ITS preamble, SLSS
  time sharing between systems based on GNSS timing
In addition, short-term coexistence solutions could be used, but are not within the scope of the current V2X SI:
  Wideband transmissions using interlacing e.g. as in UL LAA
  Sensing based approach (LBT)
RAN1 has not conducted any evaluation for some of the solutions.
RAN1 respectfully asks RAN to provide RAN1 findings to other SDOs