## Slide 1: Way Forward on eMBMS enhancements
Ericsson, Qualcomm, BBC, EBU, Nokia, ASB, Dish, AT&T, Telstra, Fraunhofer IIS
R1-165846
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23rd - 27th May 2016
Agenda item 6.2.5.1

## Slide 2: Proposal
  If a carrier is operated with 100% MBSFN subframe allocation, a single CP longer than or equal to 100us is supported
    It is understood 100% MBSFN subframe allocation is before allowing for subframes set aside for e.g. cell search, SI
    100% MBSFN subframe allocation applies to objective b), and objective d) if specified
    This carrier does not have unicast control in the MBSFN subframes
      FFS: Where to indicate MCCH change notifaction
  For a carrier that is operated with 100% MBSFN subframe allocation, legacy CPs are supported
    FFS whether it is needed to have unicast control on this carrier
  FFS whether the longer CP numerology can be supported in carriers with less than 100% MBSFN subframe allocation

## Slide 3: Proposal
  If a carrier supports mixed unicast and MBMS, at least subframes 0 and 5 of each radio frame are non-MBSFN subframes
  eMBMS enhancements do not require changes to any channels and signals needed for MBMS operation except PMCH and MBSFN-RS
    FFS whether use of more REs, TTI extension and/or change in payload are needed for PBCH coverage enhancements.