## Slide 1: Way forward on mMTC evaluation assumptions
Huawei, HiSilicon, […]
3GPP TSG RAN WG1 Meeting #85 R1-165848
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 7.1.2

## Slide 2: Background
In RAN1#85, SLS evaluation assumptions for mMTC scenario for multiple access study was agreed.
Those assumptions could be used as mMTC general assumptions.

## Slide 3: Proposal
(NOTE: this table is for UL simulation)
Attributes | Values or assumptions
Layout | Single layer - Macro layer: Hex. Grid
Inter-BS distance | 1732m
Carrier frequency | 700MHz
Simulation bandwidth | Companies report simulation bandwidth used in evaluation
Channel model | 3D UMa Take 5GCM output into account if applicable.
Tx power | UE: Max 23dBm or optional 10dBm
BS antenna configuration | Rx: 2 and 4 ports (8 as optional)
BS antenna pattern | Follow the modeling of TR36.873
BS antenna height | 25m
BS antenna tilt | Companies report tilt
BS antenna element gain + connector loss | 8 dBi, including 3dB cable loss
BS receiver noise figure | 5 dB
UE antenna elements | 1Tx
UE antenna height | 1.5m
UE antenna gain | -4dBi
Traffic model | Non-full buffer small packet. Consider future trend of mMTC traffic
UE distribution | 20% of users are outdoor in cars (100km/h) or 20% of users are outdoors (3km/h) 80% of users are indoor (3km/h) Users dropped uniformly in entire cell
BS receiver | MMSE-IRC as baseline, Advanced receiver is not precluded
UL power control | Companies report power control scheme
Channel estimation | Realistic