## Slide 1
3GPP TSG RAN WG1 Meeting #85bis R1-165857
Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.3
Summary and Observations on Simulation Results in Case 1a, 1b and 2
Spreadtrum,Orange, National Taiwan University, ZTE

## Slide 2: Background (1/2)
Agreed in RAN-1 84 bis:
  Case 1a, 1b: single numerology case
    1a: Downlink
    1b: Uplink, only one UE with narrow bandwidth is located at the edge of wide frequency band. It is assumed that no wide-band filter upon the whole frequency band.
  Case 2: DL mixed numerology case
  Case 3: UL single numerology case (asynchronous reception between UEs)
  Case 4: UL mixed numerology case (synchronous reception between UEs).

## Slide 3: Background (2/2)
In RAN-1 85, simulation results on Case 1a, 1b and 2 have been provided by many companies.
Many companies compared performance of new waveforms with that of CP-OFDM for downlink and/or SC-FDMA for uplink.
Several companies compared performance of one new waveform only with that of another new waveform but not CP-OFDM and/or SC-FDMA.
  (Samsung: R1-163990, R1-163991; Qualcomm: R1-164685, R1-164686; InterDigital: R1-165057)
We think that at this stage, considering the argument on whether we need a new waveform and whether we need a spec non-transparent waveform, it would make more sense to compare performance of various new waveforms with that of CP-OFDM/SC-FDMA first.

## Slide 4: Proposal
Observation:
  Under the given simulation assumptions, most new waveforms discussed so far outperform CP-OFDM/DFT-S-OFDM(SC-FDMA) for Case 1a, 1b, 2.

## Slide 5: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (1/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-164028 | Mitsubishi | UW-DFT-s-OFDM | 1b | Observation 4: UW serves as CP and sufficient FER performance can be obtained by controlling length of UW
R1-164035 | Huawei, HiSilicon | f-OFDM | 1a | Observation 1: f-OFDM shows better OOBE performance even considering RF non-linearity (only PA non-linearity) and therefore better spectrum utilization.

## Slide 6: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (2/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-164035 | Huawei, HiSilicon | f-OFDM | 1b | Observation 7: In narrow bandwidth case, f-OFDM has no any performance loss caused by ISI even in rich multi-path spread channel, reaping the benefits of good OOBE.
R1-164035 | Huawei, HiSilicon | f-OFDM | 2 | Observation 10: In downlink mixed numerology case, f-OFDM has much better robustness against neighboring subband interference due to its better OOBE performance, and enable mixed numerology coexistence with much less guard tone number.

## Slide 7: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (3/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-164266 | ZTE | FB-OFDM | 1a,1b | Observation 1: PAPR performance of CP-OFDM, W-OFDM and FB-OFDM are very close to each other. Observation 2: The OOB energy of FB-OFDM falls much more rapidly than CP-OFDM Observation 3: Under the selected simulation assumptions, the BLER performances of FB-OFDM are very close to (or almost the same as) that of CP-OFDM Observation 4: The smaller system guard band or less guard-tones required by FB-OFDM contributes to its higher spectrum efficiency than CP-OFDM

## Slide 8: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (4/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-164588 | Spreadtrum | FBMC-OQAM | 1a | Observation 1: FBMC shows a close BLER compared to CP-OFDM, under case 1a.
 |  |  | 1b | Observation 3: FBMC shows a close BLER compared to CP-OFDM, under case 1b
 |  |  | 2 | Observation 5: Interference from a different numerology brings CP-OFDM around 0.3dB loss, under case 2 Observation 6: FBMC shows a close performance compared to non-interfered CP-OFDM, under case 2.

## Slide 9: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (5/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-164620 | Orange | FC-OFDM | 1a, 1b, 2 | Observation 1: for case 1a, FC-ODFM and CP-OFDM provide similar performance. Observation 2: for case 1b, FC-ODFM and DFT-s-OFDM provide similar performance. Moreover, high MCS, e.g. 64QAM ¾ cannot support high mobility, and it results in error floor for long DS case, e.g. TDLc with 1000 ns. Observation 3: for case 2, FC-ODFM outperforms CP-OFDM in all MCS for all combination of channel models and velocities. The performance gain for low MCS, i.e. 16QAM ½, is not less significant than that of for high MCS, i.e. 64QAM ¾. The gain ranges from 0 dB up to infinite.

## Slide 10: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (5/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-165161 | MediaTek | f-OFDM | 2 | Observation: Under multi-numerology scenarios and with no interference mitigation efforts on the receiver side, F-OFDM does not show performance improvement over CP-OFDM for users with larger subcarrier spacing.
R1-165114 | National Taiwan University | eGFDM (CPS-OFDM) | 1a, 1b | Observation: (not quoted, but confirmed with NTU) eGFDM (CPS-OFDM) achieves much lower OOBE than CP-OFDM and enjoys potential advantages of non-orthogonality among subcarriers. (CPS: Circularly pulse-shaped)

## Slide 11: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (6/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-164655 | Sony | f-OFDM | 1a | Observation 2 : Filtered waveform reduces the out-of-band leakage compared to the OFDM. Observation 3 : Filtered waveform result is almost same as OFDM result except in higher order modulation and coding rate. Observation 4 : For higher order modulation and coding rate, BLER is worse than OFDM. Observation 5 : For higher order modulation and coding rate, BLER can be improved by adding the GI. Observation 6 : Filtered waveform increases the PAPR compared to OFDM.

## Slide 12: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (7/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-165173 | NTT DoCoMO | UF-OFDM, f-OFDM, W-OFDM | 1a, 1b | Observation 3: For Cases 1a and 1b, both FDD and TDD: • UF-OFDM shows best performance, probably due to the avoidance of power waste by using zero padding instead of CP • f-OFDM shows some degradation in Case 1b if no or small tone offset is assumed, but good performance in Case 1a • W-OFDM shows good performance in all cases
 |  |  | 2 | Observation 4: For Case 2 • For 16-QAM and 64-QAM all waveform show similar performance, both FDD and TDD • For 256-QAM CP-OFDM and UF-OFDM show worst performance due to high interference from neighbouring user, both FDD and TDD • For FDD and 256-QAM f-OFDM shows good performance, W-OFDM shows reasonable performance, for TDD W-OFDM and f-OFDM show similarly good performance

## Slide 13: Summary of Performance Evaluation for Case 1a/1b/2 compared to CP-OFDM/SC-FDMA (8/8)
T-doc number | Company | Waveform | Case | Quoted Observation on perf. compared to CP-OFDM/SC-FDMA
R1-165261 | Nokia, ALU Shanghai Bell | subb.-filt. OFDM | 1b | Observation: With 64-QAM modulation subband-filtered OFDM parameterization B4 and A4f show degraded performance at 0.1 BLER level with respect to CP-OFDM. With 256-QAM parameterization B4 is not usable, A4f and C2 show clear degradation, and C5 small degradation with respect to CP-OFDM at 0.1 BLER level. Parameterization A4h and WOLA show similar performance as CP-OFDM.