## Slide 1: Way forward on remaining issues on multiple access evaluation assumptions
Huawei, HiSilicon, […]
3GPP TSG RAN WG1 Meeting #85 R1-165875
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 7.1.2

## Slide 2: Background
In RAN1#84bis, evaluation method, metrics, scenarios, and preliminary LLS evaluation assumptions were agreed.
Email discussions [84b-11] LLS assumptions for multiple access for NR and [84b-12] SLS assumptions for multiple access for NR were conducted, and further agreements on some LLS parameters were achieved.
Remaining issues on LLS and SLS parameters needs to be addressed in RAN1#85:
  Further discussion on key parameters for LLS, e.g., target spectral efficiency per user and total allocated bandwidth.
  SLS detailed parameters for identified scenarios and other SLS related issues.

## Slide 3: Proposal
  PHY abstraction of LLS is provided for calibration purpose
  LLS results with comparison to LTE OFDMA
    Comparison should be based on the same number of users, the same total allocated bandwidth, and the same target per-user spectral efficiency
  LLS evaluation with ideal and realistic channel estimation

## Slide 4: Proposal (SLS parameters)
SLS parameters for eMBB scenario – Rural
Attributes | Values or assumptions
Layout | Single layer - Macro layer: Hex. Grid
Inter-BS distance | 1732m
Carrier frequency | 700 MHz
Simulation bandwidth | 20MHz
Channel model | RMa
Tx power | BS: 49dBm / 20MHz UE: Max 23dBm
BS antenna configuration | 2/4/8 Tx/Rx ports as start point,
BS antenna pattern | Follow the modeling of TR36.873
BS antenna tilt | Companies report tilt
BS antenna height | 35 m
BS antenna element gain + connector loss | 8 dBi
BS receiver noise figure | 5 dB
UE antenna elements | 1 Tx and 2 Rx as starting point
UE antenna height | 1.5m
UE antenna gain | Follow the modeling of TR36.873
UE receiver noise figure | 9 dB
Traffic model | For TRP spectrum efficiency: full buffer For user experienced data rate: non-full buffer; FTP model 1/3
Traffic load (Resource utilization) | 25%, 50%, 80% (other value is not precluded)， Packet size: 0.5MB; 0.1MB; other values not precluded
UE distribution | Uniform distribution, 10, 20 users per TRP or more for full buffer traffic 50% outdoor vehicles (120km/h) and 50% indoor (3km/h)
UE receiver | Advanced receiver can be considered
BS receiver | Advanced receiver can be considered
Feedback | Realistic
Channel estimation | Realistic*
*NOTE: ideal channel estimation results for calibration

## Slide 5: Proposal (SLS parameters)
SLS parameters for eMBB scenario – Dense urban
Attributes | Values or assumptions
Layout | Single layer - Macro layer: Hex. Grid Two layer is not precluded
Inter-BS distance | 200m
Carrier frequency | Around 4 GHz
Simulation bandwidth | 20MHz
Channel model | 3D UMa (Macro layer)
Tx power | BS: Macro layer: 44 dBm / 20MHz UE: Max 23dBm
BS antenna configuration | 2/4/8 Tx /Rx ports as start point, other number of antenna ports is not precluded.
BS antenna pattern | Follow the modeling of TR36.873
BS antenna height | 25m for macro cells
BS antenna tilt | Companies report tilt
BS antenna element gain + connector loss | 8 dBi
BS receiver noise figure | 5 dB
UE antenna elements | 1 Tx and 2 Rx as starting point
UE antenna height | Follow TR36.873
UE antenna gain | Follow the modeling of TR36.873
UE receiver noise figure | 9 dB
Traffic model | For TRP spectrum efficiency: full buffer For user experienced data rate: non-full buffer; FTP model 1/3
Traffic load (Resource utilization) | 25%, 50%, 80% (other value is not precluded)， Packet size: 0.5MB; 0.1MB; other values not precluded
UE distribution | Uniform distribution, 10, 20 users per TRP or more for full buffer traffic 80% indoor (3km/h), 20% outdoor (30km/h)
UE receiver | Advanced receiver can be considered
BS receiver | Advanced receiver can be considered
Feedback | Realistic
Channel estimation | Realistic*
*NOTE: ideal channel estimation results for calibration

## Slide 6: Proposal (LLS parameters)
  Further LLS evaluation with more aligned parameters are needed
    The remaining parameters such as target spectral efficiency should be chosen to reflect the typical values in SLS
Parameters | Values or assumptions
Suggested target spectral efficiency Definition: required transmission bits per user / total number of resource elements shared for data transmission | Companies need to report the values of target spectral efficiency. Initial range: 0.05bps/Hz ~ 0.5bps/Hz Other values are not precluded (Companies should justify the selection of the values).
Table 1: Additional parameters for UL

## Slide 7: Proposal
  The following should be used as performance evaluation baseline for UL grant-free/contention based multiple access studies:
    LTE OFDMA with grant-free/contention based transmissions as adopted in the proposed multiple access scheme