## Slide 1
3GPP TSG-RAN1 Meeting #85 R1-165905
Nanjing, P.R. China, 23rd- 27th May 2016
WF on the antenna port and QCL assumption study in NR
Intel, Ericsson, …
Agenda item: 7.1.6

## Slide 2: Background
Antenna port definition in LTE:
The antenna port in NR is used for transmission of a physical channel or signal, where an antenna port is defined such that the channel over which a symbol on the antenna port is conveyed can be inferred from the channel over which another symbol on the same antenna port is conveyed.
Quasi co-location (QCL) definition QCL in LTE:
Two antenna ports in NR are said to be quasi co-located if the large-scale properties of the channel over which a symbol on one antenna port is conveyed can be inferred from the channel over which a symbol on the other antenna port is conveyed. The large-scale properties include one or more of delay spread, Doppler spread, Doppler shift, average gain, and average delay.

## Slide 3: Proposal
Study QCL issue for antenna ports and antenna port measurement resource assumptions for NR
  Detailed scope of the study is provided below

## Slide 4: Proposal: Antenna port study
As a starting point for NR study RAN1 assumes the same antenna port definition as in LTE
For antenna port transmitted in different time occasions or for antenna port transmitted in the same time occasion on different frequency resource units the following issues to be studied in RAN1
Definition of time occasion and frequency resource unit for antenna port
For antenna port transmitted in different time occasions whether or not the channel on the antenna port in one time occasion can be inferred from the channel on the same antenna port in another time occasion
For antenna port transmitted in the same time occasion on different frequency resource units, whether or not the channel in one frequency resource unit on one antenna port can inferred from the channel on the same antenna port in another frequency resource unit in the same time occasion
For the cases when channel on antenna port can or can not be inferred study whether it should be fixed in the specification or signaled by network explicitly or implicitly and if signaled the required parameters

## Slide 5: Proposal: Quasi co-location (QCL) study
As a starting point for NR study RAN1 assumes the same QCL definition as in LTE.
For antenna ports corresponding to different RS types or antenna ports corresponding multiple RS of the same type or antenna ports corresponding to the same RS type the following issues to be studied in RAN1:
For antenna ports corresponding to different RS types (e.g. DM-RS and CSI-RS) or multiple RS of the same type (e.g. two NZP CSI-RS) whether or not receiver can assume QCL-ion between the antenna ports wrt to delay spread, Doppler spread, Doppler shift, average gain, and average delay.
For antenna ports corresponding to the same type (e.g. DM-RS antenna ports), whether or not receiver can assume QCL-ion between antenna ports wrt to delay spread, Doppler spread, Doppler shift, average gain, and average delay.
For case when QCL-ion or non QCL-ion is established whether it should be fixed in the specification or signaled by network explicitly or implicitly with corresponding parameters