## Slide 1: WF on further evaluation assumptions for NR waveform 30GHz and beyond
Nokia, Intel, [Samsung], [Qualcomm],[Huawei, HiSilicon],..
3GPP TSG RAN WG1 Meeting #85 R1-165914
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 7.1.3.1

## Slide 2: Proposal
Assumptions , | Value
Carrier frequency | 30 GHz & 70 GHz
Duplexing | TDD
Simulation Case | Case 1a /1b
System bandwidth | 30 GHz: 80 MHz or above, 70 GHz: 500MHz or above, other values are not precluded.
Data Bandwidth | DL: Same as system bandwidth UL: 4PRBs (48 subcarriers) or same as the system bandwidth
Numerology | FFS: Depend on numerology progress (subframe duration, Guard time interval, # of symbols per subframe, subcarrier spacing if needed)
UE antenna model | (M,N,P,Mg,Ng) = (2, 4, 2, 1, 1)
TRP antenna model | (M,N,P,Mg,Ng) = (8, 8, 2, 1, 1) Option 1: a single TXRU is mapped per panel per polarization.
Phase noise model | Follow the agreement in R1-165685
Channel coding | LTE Turbo code, other coding scheme is not preclude
Rank per UE | Rank 1-2
MCS | BPSK(pi/2), QPSK(pi/4) QPSK: 1/2, 16QAM: 1/2 or 2/3; 64QAM: 1/2 or 3/4; 256QAM: 1/2 or ¾
Control overhead | To be reported
Channel estimation | Ideal, Realistic* (Pilot pattern to be given in the case of real channel estimation)
Channel model | CDLs in TR 38.900 Delay spread scaling : {30,100} ns for 30GHz, {10,30} ns for 70GHz 3km/h, 30km/h (optional) Beam pattern used for spatial filtering needs to be reported
Table 1 Parameters for high frequency bands
NOTE: * For realistic channel estimation, the current LTE UL DMRS is recommended. Pilot overheads should be considered into the calculation of user spectrum efficiency.
* * Power-delay profiles of CDL-{A,B,C} are scenario agnostic.