## Slide 1
3GPP TSG RAN WG1 Meeting #85 R1-165917
Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.2
Way forward on High Speed Link Level evaluation
Cohere, AT&T, CMCC, Deutsche Telekom, InterDigital, Orange, Spreadtrum, Telefonica, Telstra

## Slide 2: Motivation
It has been agreed that link level evaluation is needed for the high speed train scenario (R1-165576)
Highway and V2X scenarios also require high speed to be studied
Waveform candidates should be evaluated in one or more high speed scenarios

## Slide 3: Proposal
NR waveform evaluation should include performance assessment in high speed scenarios
  Compute user spectral efficiency per definition in R1-163897

## Slide 4: Proposal: LLS evaluation assumptions for high speed
Assumptions | Value
Carrier frequency | 4 GHz
Duplex Mode | FDD/TDD
System BW | 10 MHz
Allocated BW | 4, 50 PRBs
Antenna configuration | 1x1, 2x2
Spatial precoding | Open loop [Companies should describe precoding scheme]
MCS | QPSK R=1/2, 16QAM R=1/2
Performance metric | Spectral efficiency (bps/Hz)
Mobility | 500 km/h
Numerology | Companies should describe selected numerology
Control overhead | None
Channel Estimation | Realistic (describe pilot arrangement)
Channel Model | TDL-C, ITU Rural Macro