## Slide 1: WF on semi-persistent transmission for mode 2
Ericsson, Qualcomm
3GPP TSG RAN WG1 Meeting #85 R1-165957
Nanjing, China, 23rd - 27th May 2016
Agenda item: 6.2.2.2

## Slide 2: Background
CAM traffic is not totally periodic
  Perfect prediction of future packet arrivals (at tx buffer) is not possible
RAN1 has agreed to sensing-based autonomous resource selection
  Sensing-based autonomous RA only works fine if traffic is predictable

## Slide 3: Background
Proposals booking a single resource in the future:
  ‘e’ is a single value. Examples:
    ‘e=100 ms’ or ‘e=300 ms’
  Advantages:
    UE minimizes amount of booked resources
  Disadvantages:
    If UE receives packets not aligned with transmission opportunities, either
      Latency requirement is not met
      UE transmission happens on “unpredictable” resources
Single booking (e.g. 300 ms)

## Slide 4: Background
Proposals booking multiple resource in the future
  ‘e’ is a multiple values. Examples:
    e={100,200,300,…}
      Advantages:
        UE meets 100 ms latency requirement for any packet arrival.
        UE transmissions happen on “predictable” resources
      Disadvantages: UE may book many more resources than it actually uses.
    e={300,600,900,…}
      Advantages: UE books smaller number of resources
      Disadvantages:
        If UE receives packets not aligned with transmission opportunities, either
          Latency requirement is not met
          UE transmission happens on “unpredictable” resources
    If UE switches periodicities, status of old bookings is unclear.
Multiple booking (e.g., every 100 ms)

## Slide 5: Compromise Proposal
  A UE indicates that it intends to reuse (for potential transmission) the frequency resource signaled for transmission in the SA with a period of 100ms
    e = d + k*100 ms (k=1,2,…)
    FFS terminating conditions (e.g., timeout, explicit release, underutilization, etc.)
  UE signals in SA the predicted time of its next transmission (e.g., k=3 for transmission in 300 ms)
    Maximum value of k = 10
    Time for next transmission prediction is specified as a function of arrival time of previous packets
      Details FFS
    Receiver UE uses this information
      The eNB/pre-configuration may configure UEs to ignore this information
      FFS other details

## Slide 6: Illustration of proposal
UE books multiple resources (blue) with 100 ms periodicity
UE highlights a single resource (red)
  Resource is selected based on predicted arrival for next packet
Possible RX UE behavior (FFS):
  Highlighted resource is unavailable for TX
  Other booked resource are avoided for TX (if possible)
  Advantages:
    Packets arriving at unpredicted times are still transmitted on “predictable” resources
    Booked resources (blue) can be used by other UEs if congestion is high
  Disadvantages:
SA (+data)
Resource signaled for next predicted transmission
Resource indicated for potential future use
Resource indicated for potential future use
Resource indicated for potential future use