## Slide 1: WF on channel coding simulation data sharing
Qualcomm
3GPP TSG RAN WG1 #85 R1-165959
Nanjing, China
23rd – 27th May 2016
Agenda item: 7.1.5
Document for decision

## Slide 2: Proposal
  Include file format of results with contribution
    Use excel file template provided in ExampleResults.xlsx
    Multiple columns for
      QAM, Rate, Info. Blocklength, Es/N0, BLER
    Separate tab to provide context
      Contribution#, name of code, decoder implementation, #iterations or list size, name of code construction, name of rate matching algorithm, #CRC bits, and other parameters
  Companies encouraged to submit with their contribution for RAN1 #86

## Slide 3: Example comparison from RAN1 #85
Important notes
  Complexity assumptions are not reported below and not aligned
  Plots below have not been cross simulated b/w companies
Chart: SNR to Achieve BLER=1% for QPSK R=1/5
| 100 | 400 | 1000 | 2000 | 4000 | 6000 | 8000
Polar (R1-164377) | -2.7294 | -3.2294 | -3.4794 | -3.6794 | -3.7794 | -3.8794 | -3.9294
Turbo (R1-164186) | -2 | -2.7 | -3 | -3.1 | -3.2 | -3.2
LDPC (R1-164698) | -2.2 | -3.3 | -3.7 | -3.9 | -4 | -4.1 | -4.1
Turbo (R1-164358) | 1.3206 | -0.7794 | -1.8794 | -2.5794 | -2.9794 | -3.1794 | -3.3794 | -3.5794 | -3.7294 | -3.7794
Chart: SNR to Achieve BLER=1% for 64-QAM R=8/9
| 100 | 400 | 1000 | 2000 | 4000 | 6000 | 8000
Polar (R1-164377) | 18.97 | 18.77 | 18.52 | 18.52 | 18.37
Turbo (R1-164186) | 21.8 | 19.75 | 19.75 | 18.9 | 18.85 | 18.85
LDPC (R1-164698) | 21.19 | 19.65 | 18.97 | 18.61 | 18.35 | 18.2 | 18.11
Purpose is to facilitate comparison (with proper context) among companies