## Slide 1: Way forward on remaining issues on SLS parameters for multiple access
Huawei, HiSilicon, CATT, Orange, NTT DOCOMO, VDF
3GPP TSG RAN WG1 Meeting #85 R1-166006
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 7.1.2

## Slide 2: Proposal
For rural scenario:
  Carrier frequency: 700MHz;
  ISD: 1732m;
  BS antenna configuration: 2/4/8 ports
  UE antenna configuration: 2Tx/1Tx port, 2Rx/4Rx ports;
  Traffic model:
    For spectral efficiency: full buffer (NOTE)
    For user experienced data rate: FTP model 1/3
  UE density:
    Full buffer: 10 UE per TRP, other values are not precluded;
  Traffic load (FTP)
    50%, 80%, 25% (optional)
NOTE: full buffer evaluation is not used for technical scheme down selection.

## Slide 3: Proposal
For dense urban scenario:
  Layout: Signal layer; Two layers not precluded
  BS antenna configuration: 4 or more ports
  UE antenna configuration: 2Tx/1Tx port, 2Rx/4Rx ports;
  Traffic model:
    For spectral efficiency: full buffer (NOTE)
    For user experienced data rate: FTP model 1/3
  UE density:
    Full buffer: 10 UE per TRP, 20 or other values are not precluded;
  Traffic load (FTP)
    50%, 80%, 25% (optional)
NOTE: full buffer evaluation is not used for technical scheme down selection.