## Slide 1: WF on Remaining Evaluation Assumptions
NTT DOCOMO, Intel
3GPP TSG RAN WG1 Meeting #85
Nanjing, China 23rd - 27th May 2016
Agenda item: 7.1.2
R1-166007

## Slide 2: Proposal (Dense urban)
 | Dense urban
UE distribution | Step1 (Note 1): Uniform/macro TRP (10 users per TRP for full buffer traffic) Step2 (Note 1): Uniform/macro TRP + Clustered/micro TRP (10 users per TRP associated with macro cell geographical area for full buffer traffic. 2/3 users randomly and uniformly dropped within the clusters, 1/3 users randomly and uniformly dropped throughout the macro geographical area for FTP model 1/2/3, and 60 users for FTP model 2/3) (Note 2) 80% indoor (3km/h), 20% outdoor (30km/h) (In the case of full buffer, 10 users per TRP is the baseline . 20 users per TRP is not precluded.) NOTE: In case of outdoor (30km/h), penetration loss in-car is 9 dB (LN, σ = 5 dB).
Proposal 2: Add the following note applicable to all scenarios
NOTE: Overhead should be provided by the companies
Proposal 1: Capture the followings
Note 1: Step 1 shall be used for the evaluation of spectral efficiency KPIs. Step2 shall be used for the evaluation of the other deployment scenario dependant KPIs.
Note 2: Companies are encouraged to investigate the ratio of UEs between the macro and micro cell geographical area depending on options for micro cell dropping