## Slide 1: Way forward on power amplifier assumptions for NR waveform evaluations
Nokia, ASB
3GPP TSG RAN WG1 Meeting #85 R1-166010
Nanjing, China, 23th – 27th May2016
Agenda Item: 7.1.2

## Slide 2: Background
In meeting #84bis RAN1 send an LS to RAN4 requesting information regarding realistic power amplifier assumptions for NR waveform evaluations
RAN4 provided a response to RAN1 in R1-166004 to this meeting (RAN1#85)

## Slide 3: Proposals in the RAN4 LS to RAN1
Proposal 1: For the RAN1 evaluations and simulations above 6GHz, RAN4 has not really investigated how suitable the Rapp model is for modeling the challenges facing the PA design such as low efficiency, high frequency, and wide channel bandwidth, etc. Nevertheless, the Rapp model is considered a better model than the clipping model. The Polynomial model suggested for below 6 GHz can also be re-used for above 6GHz and would be better than Rapp. RAN4 is still looking into more accurate PA modelling like the impact of memory effect for higher frequencies and wider bandwidths as intended by NR.
Proposal 2: For the RAN1 evaluations and simulations below 6 GHz LTE and Wi-Fi PA measurements results with candidate waveforms shall serve as the benchmark for modelling. RAN4 propose the following model based on real measurement using AM/AM and AM/PM polynomial approximation for initial studies:
PA output y(t) to be computed from input x(t) using the formula y(t) = p0 + p1∙x(t) + p2∙x(t)2 + p3∙x(t)3 + …
The coefficients are organized as follows: [p9 p8 p7 … p0] and the
p_am = [7.9726e-12 1.2771e-9 8.2526e-8 2.6615e-6 3.9727e-5 2.7715e-5 -7.1100e-3 -7.9183e-2 8.2921e-1 27.3535];
p_pm = [9.8591e-11 1.3544e-8 7.2970e-7 1.8757e-5 1.9730e-4 -7.5352e-4 -3.6477e-2 -2.7752e-1 -1.6672e-2 79.1553]

## Slide 4: Proposal
It is proposed that RAN1 adopts the models provided in RAN4 LS to the NR waveform evaluations