## Slide 1
3GPP TSG RAN WG1 Meeting #85bis R1-165665
Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.3
Definition of OFDM based waveform
Spreadtrum, Orange, Sony, Cohere, NTU, [Qualcomm] …

## Slide 2: Background
Agreed in RAN-1 84bis:
  Waveform is based on OFDM
    Multiple numerologies are supported
    Additional functionality on top of OFDM such as DFT-S-OFDM, and/or variants of DFT-S-OFDM, and/or filtering/windowing, and/or OTFS is further considered
      Complementary non-OFDM based waveform is not precluded for some specific use cases (e.g., mMTC use case)
The definition of what is a OFDM-base waveform is not very clear yet

## Slide 3: Proposal 1
Definition: An OFDM-based waveform is a waveform based on IDFT(IFFT) operation.
  Includes at least CP-OFDM, OFDM-WOLA, f-OFDM, FB-OFDM, UFMC, GFDM, W-OFDM, FBMC-OQAM, FC-OFDM, UW DFT-S-OFDM, GI DFT-S-OFDM, DFT-S-OFDM, variants of DFT-S-OFDM, OTFS, etc.

## Slide 4: Reference
“On Waveform Design for 5G”: https://www.qualcomm.com/documents/5g-waveform-multiple-access-techniques, in R1-162199 (Qualcomm)