## Slide 1: WF on Supporting different Numerologies in a NR carrier
LG Electronics, Huawei, HiSilicon, Panasonic,
3GPP TSG RAN WG1 Meeting #85 R1-165837
Nanjing, China, 23th – 27th May 2016
Agenda Item: 7.1.1

## Slide 2: Background
Agreements from Tuesday:
  Forward compatibility of NR shall ensure smooth introduction of future services and features with no impact on the access of earlier services and UEs
    Multiplexing different numerologies within a same NR carrier bandwidth (from the network perspective) is supported
      FDM and/or TDM multiplexing can be considered

## Slide 3: Proposal
Contiguous frequency resources using one numerology set in a NR carrier is called ‘FRG’
  A numerology set is defined by CP duration and subcarrier spacing
  Multiple FRGs in a NR carrier is supported
  Multiple FRGs in discontinuous frequency resources in a NR carrier can use the same numerology set
  NR supports the following
    Each FRG has independent synchronization signal(s)
    Multiple FRGs share the same synchronization signal(s)
  FFS
    sizes of FRG
    whether FRG (including size of FRG) can change dynamically or semi-statically.
    whether different FRGs can overlap or not
    whether/how to handle DC subcarrier aspects in a NR carrier comprising multiple FRGs