## Slide 1: WF on antenna placement in Indoor scenarios
Intel, NTT DoCoMo, Samsung, Ericsson
R1-165850
3GPP TSG RAN1 #85
Nanjing, China, May 23 - 27, 2016
Agenda Item: 7.1.2

## Slide 2: Background
In R1-163861, indoor hotspot, dense urban, urban macro and rural macro scenarios are agreed
In R1-163885, antenna modelling for NR has been agreed
This WF address the missing details of TRP antenna modelling for indoor Open-Office scenario

## Slide 3: Proposal
RAN1 to study different TRP numbers and deployment options for Indoor Open-Office scenario
  Candidate TRP numbers: 3, 6, 12
  Deployment options: wall-mount, ceiling-mount and 3-sector based as shown in the following pages
  Company shall provide details of antenna pattern and sector orientations

## Slide 4: Alternative 1 of TRP antenna modeling for indoor Open-Office scenario
Antenna element radiation pattern in dim (dB) | =25
Antenna element radiation pattern in dim (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element | [5dBi]
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element | [5dBi]
Single sector omni in azimuth dimension and 130 degree 3dB beamwidth in zenith dimension. Detailed antenna element radiation pattern according to below table. Electrical tilting is FFS.

## Slide 5: Alternative 2 of TRP antenna modeling for indoor Open-Office scenario
Antenna element radiation pattern in dim (dB) | =25
Antenna element radiation pattern in dim (dB) | =25
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element | [8dBi]
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element | [8dBi]
Three sectors and each sector has 65 degree 3dB beam width in both zenith and azimuth dimensions. Detailed antenna element radiation pattern according to below table. [110] degree electrical tilting.

## Slide 6: Alternative 3 of TRP antenna modeling for indoor Open-Office scenario
Antenna element radiation pattern in dim (dB) | =25
Antenna element radiation pattern in dim (dB) | =25
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element | 5dBi
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element | 5dBi
TRP is placed on the wall. Single sector with 90 degree 3dB beam width in both zenith and azimuth dimensions. Antenna orientation is opposite to the wall. Detailed TRP positions FFS. Electrical tilting is FFS.

## Slide 7: Alternative 4 of TRP antenna modeling for indoor Open-Office scenario
Antenna element radiation pattern in dim (dB) | =25
Antenna element radiation pattern in dim (dB) | =25
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element | [5dBi]
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element | [5dBi]
TRP is placed below the ceiling. Sector with 130 degree 3dB beam width in both zenith and azimuth dimensions. Antenna orientation is towards floor.