## Slide 1: Way forward on processing timing reduction for sTTI
Ericsson
R1-165854
AI 6.2.10.2
3GPP RAN WG 1 #85
23rd – 27th May2016, Nanjing , P.R. China

## Slide 2: Background
The system evaluation provided to RAN1 #85 shows that
  if the processing time cannot be linearly scaled with TTI length but remains close to the linearly scaled value, short TTI significantly improves data rate
  subframe long TTI with reduced processing time can improve user performance
Maximum TA affects the minimum delay between UL grant reception and UL data transmission and between the DL data reception and DL HARQ feedback transmission

## Slide 3: Proposal (1)
The minimum timing for UL grant to UL data and for DL data to DL HARQ is n + k sTTI for short TTI operation. Down-select among the following options
  Option 1
    Processing time >= the legacy processing time linearly downscaled with TTI length
      4 <= k <= 8
  Option 2
    Processing time is lower than the legacy processing time linearly downscaled with TTI length for at least slot based TTI
      k < 4 for slot based TTI.
      FFS value of k for 2os and 4 os TTI
  Note that sTTI refers to
    sPUSCH sTTI for the UL grant to UL data timing
    sPDSCH sTTI for the DL data to DL HARQ feedback timing
Further study whether or not the eNB would indicate an additional allowed delay m, resulting in a timing of n + k + m sTTI
  As an example m could be utilized to handle large TA values
  FFS: semi-static or dynamic configuration of m

## Slide 4: Proposal (2)
The minimum timing for UL grant to UL data and for DL data to DL HARQ is n + k TTI for subframe-long TTI operation and short TTI capable UEs.
  k = 4 is supported
  Further study whether a reduced minimum timing is possible, e.g. k = 2, k = 3, and if a reduced maximum TBS is needed to achieve this
Note: CQI feedback enhancements for short TTI and legacy TTI are not precluded