## Slide 1: WF on Time Reference for Ack/Nack Transmission
Ericsson
R1-165884
3GPP TSG RAN WG1 meeting #84bis
Nanjing, China,23rd-27th May, 2016
Agenda item 6.1.6

## Slide 2: Background
Two Alternatives are under discussion for the time reference point of UL A/N transmission
Alt 1: Baseline time point for time domain allocation:
  A/N transmission is relative to the first time reference point which is at least 12 ms later than the end of NPDSCH
  The period of the time reference point is fixed to [2]ms.
    The start of the period is from (SFN#0, subframe#0).
Alt. 2: A/N transmission delay is relative to the end of the corresponding NPDSCH transmission plus 12ms.

## Slide 3: Background
The proponent of Alt 1 claims that in few cases that Alt1 can give better UL resource utilization. However, Alt1 has negative impacts on both latency and UE data rate (R1-164100).
The proponent of Alt2 claims that the system functions well without introducing a fixed reference point, as well as the difficulty to align the UL A/N even after introducing a fixed reference point (R1-165000).

## Slide 4: Background
The proponents of Alt1 claim that the time offset is in the range of {0, 2, 4, 6} ms for 15kHz ACK/NACK transmission may causes resource packing issues in few conditions.
This could be solved if we introduce both odd and even numbers for the time offset for 15 kHz ACK/NACK.

## Slide 5: Proposal 1
Introduce both odd and even numbers for the time offset for 15 kHz ACK/NACK.

## Slide 6: Proposal 2
It is proposed to use the following values in the DCI instead of {0, 2, 4, 6} ms for 15kHz ACK/NACK transmission.
  Alt1 {0 1 4 5}
  Alt2 {0 2 3 5}
  Alt3 {0 2 4 5}
  Alt4 other values