## Slide 1: WF on priority handling for V2V
3GPP TSG RAN WG1 Meeting #85 R1-16xxxx
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 6.2.2.2.4
Huawei, HiSilicon, Intel, Ericsson, Sharp, LG Electronics, NTT DoCoMo, OPPO , ITRI, Kyocera, Nokia, ASB, Potevio, Sony, ZTE, III, CATT, Samsung

## Slide 2: Background
Agreements on priority handling in RAN1 #84bis:
  Proposal 1:
    Priority handling is supported over PC5 for eNB-scheduled and UE- autonomous V2V communication
  Proposal 2:
    The priority information is taken into account in the resource (re)selection for UE-autonomous mode
      Further details are FFS
  Proposal 3:
    Down-select between two alternatives at RAN1#85 meeting
      Alt.1 Priority information is signaled in SCI
      Alt.2 Priority information is not signaled in SCI

## Slide 3: Proposal
If UE intending to transmit a packet with a given priority detects a transmission intention of another UE’s packet with higher priority information on the same resource based on sensing, the UE does not transmit on the resource and (re)selects other resource.
  FFS if additional criteria is needed
  FFS how to obtain the priority information