## Slide 1: WF on time resources indication
Huawei, HiSilicon, LGE, Ericsson
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, 22nd - 26th Aug., 2016
AI: 7.2.2.3
R1-167925

## Slide 2: Background
In Rel-12 D2D, T-RPT is included in SA to indicate all the time resources used for (re)transmissions corresponding to one TB or multiple TBs.
For V2V, having time resource indication of one TB in SA is beneficial
  A UE can obtain all time resource indication corresponding to all one TB (re)transmissions once a single SA is successfully received.
  For sensing, decoding one SA can recover reservation information corresponding to all one TB (re)transmissions
  For V2V mode 1, time resource indication of one TB carried in sidelink DCI can be directly reused in SCI.

## Slide 3: Proposal
  The time resources of all the data transmissions corresponding to the same TB are indicated by each SA of these transmissions.
  The time resources indicated in SA only corresponds to one TB transmission.

## Slide 4: Example
Step 2 PSSCH resource exclusion based on time resource indication