## Slide 1: WF on beam management
Intel Corporation, Ericsson…
R1-167950
3GPP TSG RAN1 #86
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda Item: 8.1.5

## Slide 2: Proposal
Distinguish two beam related procedures:
  Procedure A is used to support beam based mobility
    Main purpose is to discover TRP TX beams and perform mobility related measurements
    UE RX beam training support may also be considered
    Searching and discovering TRP TX beams from neighbor TRPs which are non-synchronized is supported
      Note: TRPs may still be synchronized but the UE shall not make such assumption
    L3 reporting
  Procedure B is used to support beam management
    Purpose is to track TRP TX beams and support UE to select UE RX beams
    RS (beams) to measure on are explicitly configured to the UE
      Note: No search/discovery procedure is involved
    L1/L2 reporting