## Slide 1: Way forward on waveform
Huawei, HiSilicon, NTT DOCOMO, Nokia, ASB, Ericsson, Qualcomm, China Unicom, CATT, Samsung, CATR, Vodafone, InterDigital, LG Electronics, Softbank, Deutsche Telekom
3GPP TSG RAN WG1 Meeting #86 R1-167963
Gothenburg, Sweden 22nd - 26th August 2016
Agenda Item: 8.1.2.1

## Slide 2: Proposals
At least up to 40 GHz for eMBB and URLLC services, NR supports CP-OFDM based waveform with Y greater than that of LTE for DL and UL, possibly with additional low PAPR technique(s) (including DFT-S-OFDM)
  Y = transmission bandwidth configuration / channel bandwidth
  RAN1 specification will support Y up to approximately100%
  Some evaluations in RAN1 show that Y for a NR carrier can be up to 98% for both DL and UL for the evaluated channel bandwidths [R1-166093] without complexity and latency constraints
It is recommended that RAN4 should aim to support eNB/UE with Y significantly higher than 90% when defining the RAN4 requirements considering complexity and latency constraints

## Slide 3: Proposals
In-band frequency multiplexing of different numerologies is supported in NR for both DL and UL, at least from the network perspective
  It is expected that spectrum confinement on sub-band basis is specified as requirements on
    Transmitter side in-band emission and EVM requirements
    Reception performance in presence of other-subband interferer
From RAN1 perspective, spectral confinement technique(s) (e.g. filtering, windowing, etc.) at the transmitter is transparent to the receiver
Additional waveforms may be supported by NR for e.g. other services (e.g. mMTC)
Inform RAN4 the above agreements
  RAN1 plans to perform more evaluations on waveform and will inform RAN4 with future updates