## Slide 1: WF on beam management
CATT, Samsung
3GPP TSG RAN WG1 Meeting #86 R1-167966
Gothenburg, Sweden, August 22nd - 26th 2016
Agenda Item: 8.1.5

## Slide 2: Background
Channel [beam] reciprocity
  Holds for both TRP and UE
  Does not hold for TRP and UE
  Holds for TRP but does not hold for UE
  Does not hold for TRP but holds for UE

## Slide 3: Background
Definition: A beam pair consists of one Tx beam and one Rx beam in one link direction

## Slide 4: Proposal(1)
RAN1 should study beam management procedures under different channel reciprocity assumptions
  At a TRP or UE, with TX and RX channel reciprocity (e.g., beam reciprocity), TX beam (or RX beam) can be obtained from RX beam (or TX beam) to reduce overhead and latency
  Without TX and RX channel reciprocity, beam management procedure may require TX and RX beam sweeping in both DL and UL links

## Slide 5: Proposal(2)
RAN1 should study different methods of determining a beam pair for communication, e.g.,
  Joint determination: Tx beam and Rx beam of the beam pair are determined jointly
  Separate determination: Tx beam or Rx beam of the beam pair are determined sequentially

## Slide 6: Proposal(3)
Study beam management procedure with and without explicit indication of beam(s) used for data/control channel or reference signal transmission