## Slide 1: WF on Advanced CSI in Rel-14
Huawei, HiSilicon, Deutsche Telekom, China Unicom, AT&T, China Telecom
3GPP TSG RAN WG1 #86 R1-167967
Gothenburg, Sweden 22nd- 26th August, 2016
Agenda item: 7.2.4.2.3

## Slide 2: Background
  RAN1 #85 agreed to specify advanced CSI. The specified enhancement is to be selected from the following categories:
    Enhancements to Rel-13 feedback codebooks (FFS which numbers of antenna ports from the set {8, 12, 16, 20, 24, 28, 32}) that increase CSI resolution through improved beam selection / construction in W1 and/or improved beam/port selection / combining / weighting mechanisms in W2
    Parameters representing channel coefficients, or some reduced space representation thereof including beam combining / weighting with coefficient quantisation or channel quantisation or channel covariance matrix quantisation
      Uplink physical channel enhancements to carry the representation of channel coefficients can be included if selected
  Observations
    The two categories can be unified (exactly the same) if
      Reduced space (eigenvectors)/W1 is constructed on a orthogonal basis (e.g. DFT matrix)
      Reduced space representation/W2 is to further combine selected beams
      Granularity of weighting(phase and amplitude) can be either wideband or subband
    Note CQI derivation is always based on associated CSI for both of the two categories

## Slide 3: Proposals
Specify advanced CSI for {4,8,12,16,20,24,28,32} antenna ports.
Strive for the unified advanced CSI feedback framework with
  Reduced space (eigenvectors)/W1 is constructed on a orthogonal basis (e.g. DFT matrix)
  Reduced space representation/W2 is to further combine selected beams
  Granularity of weighting(phase and amplitude) can be either wideband or subband
  Introduction of a new uplink physical channel (i.e. analog feedback) to carry the advanced CSI in case
    Antenna port is {4,8}
    The amount of quantization bits is high