## Slide 1
3GPP TSG-RAN1 Meeting #86 R1-167970 Gothenburg, Sweden 22nd - 26th August 2016
WF on the antenna ports QCL in NR
Intel, LGE, Ericsson, Samsung, InterDigital, Huawei/HiSilicon
Agenda item: 8.1.5

## Slide 2: Proposal (1/3)
All physical channels and reference signals in NR are transmitted using antenna ports
Agree as working assumption the following antenna port definition for NR (same as in LTE)
  An antenna port is defined such that the channel over which a symbol on the antenna port is conveyed can be inferred from the channel over which another symbol on the same antenna port is conveyed.

## Slide 3: Proposal (2/3)
Large-scale parameters for antenna port QCL in NR includes at least
  Average gain, average delay, delay spread, Doppler shift and Doppler spread (same as in LTE)
  Additional parameters are FFS
FFS whether the QCL or other means can be used for UE beamforming management

## Slide 4: Proposal (3/3)
QCL for DM-RS antenna ports in NR
  NR should support transmission methods
    All the DMRS antenna ports are QCL-ed with each other
    Not all the DMRS antenna ports are QCL-ed with each other
    Note: QCL wrt average gain, average delay, delay spread, Doppler shift, Doppler spread
  QCL assumptions for DM-RS antenna ports for further study
    QCL across scheduled PRBs for DM-RS antenna port
    QCL among DM-RS antenna port groups
    QCL of DM-RS antenna ports with antenna ports of other reference signals (e.g. CSI-RS, or other RS to be defined in NR)
Note: The antenna ports of demodulation reference signal (DM-RS) in NR are used to transmit at least physical data and control channels and used at the UE for demodulation.