## Slide 1: WF on Advanced CSI feedback framework in Rel-14
Huawei, HiSilicon, Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, Samsung, CATT, ZTE, NTT DOCOMO, Qualcomm, Intel
3GPP TSG RAN WG1 #86 R1-167971
Gothenburg, Sweden 22nd- 26th August, 2016
Agenda item: 7.2.4.2.3

## Slide 2: Background
  RAN1 #85 agreed to specify advanced CSI. The specified enhancement is to be selected from the following categories:
    Enhancements to Rel-13 feedback codebooks (FFS which numbers of antenna ports from the set {8, 12, 16, 20, 24, 28, 32}) that increase CSI resolution through improved beam selection / construction in W1 and/or improved beam/port selection / combining / weighting mechanisms in W2
    Parameters representing channel coefficients, or some reduced space representation thereof including beam combining / weighting with coefficient quantisation or channel quantisation or channel covariance matrix quantisation
      Uplink physical channel enhancements to carry the representation of channel coefficients can be included if selected

## Slide 3: Proposals
Strive for the advanced CSI feedback framework with
  Reduced space (eigenvectors)/W1 is constructed based on one of the following alternatives (TBD RAN1#86bis):
    Alt1. Orthogonal basis (e.g. DFT matrix)
    Alt2. Non-orthogonal basis, e.g., Rel.13 Class A W1
  Reduced space representation/W2 is to further combine selected beams
  Granularity of weighting(phase and/or amplitude) can be either wideband only or wideband/subband, and is constructed based on one of the following alternatives (TBD RAN1#86bis):
    Alt1. Phase and amplitude
    Alt2. Phase-only weighting
  How the enhanced framework can be applicable for Class A and/or Class B eMIMO-Types is FFS
  FFS: How to handle the relationship between advanced CSI feedback and legacy CSI feedback framework
Companies are encouraged to provide results comparing the above alternatives, considering a mix of smaller and larger numbers of ports within the following antenna port configurations
  {4,8,12,16,20,24,28,32} ports