## Slide 1: WF on supporting larger TBS
Huawei, HiSilicon, …
3GPP TSG RAN WG1 Meeting #86 R1-167974
Gothenburg, Sweden, 22nd – 26th August
Agenda Item: 7.2.10.1

## Slide 2: Background
The available uplink subframes within one radio frame for TDD and HD-FDD will be less than 10.
  1Mbps target peak rate will be significantly decreased for UEs with 6PRB bandwidth, to around 200 kbps
  This restricts the deployment scenarios of TDD/HD-FDD for MTC applications especially for Cat. M1 UEs, even in Rel-14.
The importance of larger uplink TBS for TDD/HD-FDD was discussed thoroughly in the past meetings.
    Larger TBS can enlarge the market of supported application scenarios with negligible cost addition.

## Slide 3: Proposal
  Larger max UL TBS support is introduced as a Rel-14 capability for at least Cat. M1 BL/CE UEs
    Larger max UL TBS if the capability is indicated is X bits
      X is one value from [2984 or 3240] bits
    Larger max UL TBS only applies in connected mode, i.e. after UE capability is known
  Max UL TBS support in PUSCH BW > 6 PRB is at least X bits