## Slide 1: WF on requirements for NB-IoT positioning
Huawei, HiSilicon, …
R1-167983
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-27, 2016
Agenda item 7.2.11.1

## Slide 2: Background
The Rel-14 NB-IoT enhancements WID invites input on requirements for NB-IoT positioning
Support of UTDOA or OTDOA:
      Study accuracy, UE complexity, UE power consumption for both UTDOA and OTDOA using NB-IoT and provide recommendation to RAN#73 on which one solution to adopt [RAN1]
        3GPP network operators are invited to provide inputs to RAN1#86 on their positioning requirements. Companies are encouraged to include both methods in their evaluations.
      Based on the study make a choice (either uplink positioning or OTDOA) during RAN#73
The requirements in RAN1#86 should be sufficient to allow a recommendation to RAN. It is not necessary to design or select any specific solution in this first meeting

## Slide 3: Proposal
Horizontal accuracy of 50 m, 67% of UEs.
Accuracy target applies to stationary (i.e., 0 km/h) and pedestrian (i.e., 3 km/h) UEs as a priority, higher speed (i.e., 30 km/h and 120 km/h) UEs can also be considered if suitable solutions are found
Accuracy target applies to outdoor scenarios only.
Accuracy target met in synchronous and asynchronous networks, i.e. E-SMLC is assumed to know the absolute timing of each involved eNB
Time to determine position <= 10sec (same latency as Rel-13)
Requirements are the same for all three operation modes (i.e. stand-alone/in-band/guard band) per the WID
Low power class UEs (if introduced by RAN4) have same requirements as 20/23 dBm NB-IoT UEs, but allowing for MCL relaxations agreed by RAN4.
No need for hardware LMUs
  Software function per eNB is permitted
Other requirements as for Rel-13 NB-IoT, including
  UE signal processing effort is not increased beyond Rel-13
  Solutions with smaller total impact to UE battery life are preferred.
  Scalability to support massive UEs per cell (i.e., > 50k UEs/cell)