## Slide 1: WF on observations on performance aspects of NB-IoT positioning
Huawei, HiSilicon, …
R1-167984
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-27, 2016
Agenda item 7.2.11.1

## Slide 2: Background
The Rel-14 NB-IoT enhancements WID asks RAN1 to study both UTDOA and OTDOA for NB-IoT, and to provide recommendation to RAN#73 as the basis to make a choice
Support of UTDOA or OTDOA:
      Study accuracy, UE complexity, UE power consumption for both UTDOA and OTDOA using NB-IoT and provide recommendation to RAN#73 on which one solution to adopt [RAN1]
        3GPP network operators are invited to provide inputs to RAN1#86 on their positioning requirements. Companies are encouraged to include both methods in their evaluations.
      Based on the study make a choice (either uplink positioning or OTDOA) during RAN#73
The observations on the performance of different positioning methods is important for the recommendation.

## Slide 3: Observations
Positioning accuracy
  With properly-designed uplink positioning signal, UTDOA has been found to achieve an accuracy of 50m @ 67% at least for NB-IoT UEs with transmit power of 23 dBm for in-band, guard-band, and standalone deployment.
  OTDOA has been found to achieve an accuracy of approximately 100m @ 67% for in-band, guard-band, and standalone.
Air-interface latency
  The air-interface latency for OTDOA includes the time for measurements of serving cell and configured neighboring cells and the time for reporting measurement results.
  The air-interface latency for UTDOA includes the time for transmitting an uplink positioning signal.