## Slide 1: WF on observations on UE impact aspects of NB-IoT positioning
Huawei, HiSilicon, …
R1-167985
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-27, 2016
Agenda item 7.2.11.1

## Slide 2: Background
The Rel-14 NB-IoT enhancements WID asks RAN1 to study both UTDOA and OTDOA for NB-IoT, and to provide recommendation to RAN#73 as the basis to make a choice
Support of UTDOA or OTDOA:
      Study accuracy, UE complexity, UE power consumption for both UTDOA and OTDOA using NB-IoT and provide recommendation to RAN#73 on which one solution to adopt [RAN1]
        3GPP network operators are invited to provide inputs to RAN1#86 on their positioning requirements. Companies are encouraged to include both methods in their evaluations.
      Based on the study make a choice (either uplink positioning or OTDOA) during RAN#73
The observation on the impact of different positioning methods on UE is important for the recommendation to RAN#73.

## Slide 3: Observations
Impact to UE implementation/complexity
  For OTDOA, UE needs to support
    LTE Positioning Protocol (LPP) to communicate with E-SMLC via eNB.
    Measurements for positioning to get downlink RSTD of up to 24 configured neighboring cells.
  For UTDOA, UE does not need to support additional protocol and signal processing (e.g., measurements for positioning).
Impact to UE power consumption
  For OTDOA, the UE power consumption for positioning includes the power consumed by any DL signaling, signal processing (e.g., measurements) and UL reporting of the measurements of up to 24 configured neighboring cells for the purpose of positioning
  For UTODA, the UE power consumption for positioning includes the power consumed by transmitting UL signal for the purpose of positioning