## Slide 1: WF on observations on network impact aspects of NB-IoT positioning
Huawei, HiSilicon, …
R1-167986
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-27, 2016
Agenda item 7.2.11.1

## Slide 2: Background
The Rel-14 NB-IoT enhancements WID asks RAN1 to study both UTDOA and OTDOA for NB-IoT, and to provide recommendation to RAN#73 as the basis to make a choice
Support of UTDOA or OTDOA:
      Study accuracy, UE complexity, UE power consumption for both UTDOA and OTDOA using NB-IoT and provide recommendation to RAN#73 on which one solution to adopt [RAN1]
        3GPP network operators are invited to provide inputs to RAN1#86 on their positioning requirements. Companies are encouraged to include both methods in their evaluations.
      Based on the study make a choice (either uplink positioning or OTDOA) during RAN#73
The observation on the impact of different positioning methods on network is important for the recommendation to RAN#73.

## Slide 3: Observations
Impact to network implementation
  Enhanced Serving Mobile Location Center (E-SMLC) is needed for both UTDOA and OTDOA.
  For UTDOA, a logical element of Location Measurement Unit (LMU) is additionally introduced to implement measurement for positioning.
    Class 1 LMU can be a software function of eNB
  For OTDOA, no additional logical element is needed.
Scalability/Capacity
  For UTDOA, the uplink time-frequency resources of transmitting uplink positioning reference signal increases linearly with increased cell positioning load.
  For UTDOA, the basestation processing load (e.g., uplink measurements) increases linearly with increased positioning load.
  For OTDOA, the uplink time-frequency resources of reporting measurements increases linearly with increased positioning load.
  For OTDOA, the downlink time-frequency resources for transmitting downlink positioning reference signal may or may not increase with increased positioning load.
  For OTDOA, the basestation processing load may not increase with increased positioning load.