## Slide 1: WF on CDM aggregation for NP CSI-RS
Samsung, Xinwei, Ericsson
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 7.2.4.1.1
R1-167996

## Slide 2: Background
CDM aggregation can support core features for Rel.14 UEs
  Support flexible CSI-RS port sharing
    Between CDM-8 and CDM-2/-4
    Between Nk=4 and Nk=8
  Full power utilization for 28-/32-port CSI-RS
  Etc.

## Slide 3: Proposal
CDM aggregation between multiple CSI-RS configurations should be studied in Rel.14
  E.g. CDM-2/-4 patterns in the different CSI-RS configurations can be aggregated in order of the CSI-RS configuration index
  Ex1: Two CDM-2 patterns in the different CSI-RS configurations can be aggregated in order to achieve a CDM-4 pattern
  Ex2: Two CDM-4 patterns in the different CSI-RS configurations can be aggregated in order to achieve a CDM-8 pattern
    FFS whether this aggregation applies to {24 , 32} ports only or it applies to {20, 24, 28, 32} ports
  Details and simulation assumptions are FFS

## Slide 4: Example
PRB n |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | 15/16 |  |  |  | 22/23 |  |  | 
 |  |  |  |  |  | 19/20 |  |  |  | 26/27 |  |  | 
 |  |  |  |  |  | 17/18 |  |  |  | 24/25 |  |  | 
 |  |  |  |  |  | 20/21 |  |  |  | 28/29 |  |  | 
 | Slot 0 |  |  |  |  |  |  | Slot 1 |  |  |  |  | 
The first CDM-2 patterns of each 8-port CSI-RS configuration are aggregated into a new CDM-4 pattern