## Slide 1: WF on Channel Coding Selection for Control Channel
Huawei, HiSilicon, CMCC, CUCC, Deutsche Telekom, Orange, Telecom Italia, Vodafone, China Unicom, MTK, Interdigital, Spreadtrum
3GPP TSG RAN WG1 #86 R1-168042
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda item: 8.1.4.1

## Slide 2: Background
Channel Codes for NR control channel
  Polar code
  LTE-TBCC
  RM
Comparison
  BLER Performance
  Complexity
  False-Alarm probability of blind detection
Channel* | AWGN |  | 
Modulation | QPSK |  | 
Coding scheme | RM | TBCC | Polar
Info. Block length (DL) | 28 43 55 67 |  | 
Coded Block length (DL) | 288 576 |  | 
Info. Block length (UL) | 4 8 11 |  | 
Coded Block length (UL) | 20 24 |  | 
Decoding | ML | Viterbi | SCL-X

## Slide 3: Observations
RAN1#86 (Aug 2016)
  Under equal complexity, Polar outperforms TBCC by 1.5dB
    Legacy TBCC with Viterbi algorithm == Polar decoder with list 8 (SCL-8)
    Enhanced Polar decoder or new TBCC code can improve either by ~0.5dB at cost of more complexity, but the difference is still 1.5dB
    Summary plot on next slide [R1-167216 + list 8 results]
  For larger info block sizes, TBCC will get worse and Polar code will get better
    UCI may use several hundred bits
  Both codes have false alarm probability of e.g. 16 bit CRC
    For both codes CRC is not used for error correction, only error detection

## Slide 4: Simulation Results

## Slide 5: Way Forward
  Polar code is considered as channel coding technique for NR for control channel UL and DL
      Even a low complexity small list size polar decoder is shown to have a performance advantage over TBCC
  Further comparison of Polar and TBCC is encouraged