## Slide 1: WF on Paging on non-anchor PRBs
Qualcomm
R1-168052
3GPP TSG RAN WG1 Meeting #86
Gothemburg, Sweden, 22-26 Aug 2016
Agenda item 7.2.11

## Slide 2: Background
In RAN#72 a new work item enhancements of NB-IoT was approved
One of the objectives is:
  Support transmission of paging on a non-anchor NB-IoT PRB [RAN2, RAN1,RAN3]

## Slide 3: Background
All Rel-13 UE monitor paging in the anchor PRB.
Rel-14 UE may monitor paging in non-anchor PRB.
It is desirable to distribute Rel-14 UE in a non-uniform way among anchor and non-anchor PRB.
Also, it is desirable that monitoring is based on UE_ID to avoid unnecessary signaling to the network when the UE changes coverage (similar to eMTC).

## Slide 4: Proposal
A Rel-14 UE chooses the PRB for paging based on UE_ID
It is possible to distribute Rel-14 UEs in a non-uniform way among anchor and non-anchor PRB
  FFS exact mechanism
At least the following can be different between anchor and non-anchor PRBs for paging:
  Power boosting of NRS
  Number of repetitions for NPDCCH.
Send LS to RAN2 with these agreements