## Slide 1: WF on Clarification of Grant-free Transmission for mMTC
ZTE, ZTE Microelectronics, Qualcomm, LGE, []…
3GPP TSG RAN WG1 #86 R1-168067
Gothenburg, Sweden
22nd – 26th August 2016
Agenda item: 8.1.2.2
Document for decision

## Slide 2: Background
Autonomous/grant-free/contention based UL non-orthogonal multiple access has the following characteristics
  A transmission from UE does not need the dynamic and explicit scheduling grant from eNB
  Multiple UEs can share the same time and frequency resources

## Slide 3: Proposals
  In grant-free mode of transmission
  a UE is allowed to randomly choose a code, a sequence or an interleaver pattern from a pool known to eNB and UE beforehand
  eNB receiver should perform blind detection for user separation
    including Preamble/DMRS-based blind detection