## Slide 1: WF on UL Multiple Access Scheme Categorization for mMTC
ZTE, ZTE Microelectronics, Qualcomm,[]…
3GPP TSG RAN WG1 #86 R1-168068
Gothenburg, Sweden
22nd – 26th August 2016
Agenda item: 8.1.2.2
Document for decision

## Slide 2: Background
Examples of non-orthogonal MA schemes include (but not limited to)
It is necessary to categorize these schemes in order to reduce the simulation/evaluation workload
MA scheme | References | Key features | Receiver type
MUSA | R1-164270, R1-166404 | Short full-length code spreading | MMSE-SIC
NOCA | R1-165019, R1-167249 | Full-length code spreading | MMSE-SIC
NCMA | R1-162517, R1-166876 | Full-length code spreading | SIC/PIC
RSMA | R1-164688, R1-166358 | Full-length code spreading | RAKE/MME-SIC
Low code rate spreading | R1-162385, R1-166552 | Long code spreading or Interleaver | Various
GOCA | R1-167535, R1-167536 | Two-stage code spreading | SIC
SCMA | R1-164703, R1-166094 | Short sparse code spreading | MPA/MPA-SIC
PDMA | R1-163383, R1-167870 | Sparse code-based pattern | BP
IGMA | R1-163992, R1-166750 | Interleaver and grid mapping | ESE/MAP
RDMA | R1-167535, R1-167536 | Interleaver and repetition | SIC
NOMA | R1-163111, R1-165175 | Power domain non-orthogonality | SIC

## Slide 3: Proposals
  Grant-free non-orthogonal multiple access schemes can be categorized based on the ways to (non-orthogonally) separate users:
  Category 1: Non-structured code spreading
  Category 2: Structured code spreading
  Category 3: Interleaver based
  * Schemes with combined features across categories are not precluded
  ** Conjunction with orthogonal spreading is not precluded