## Slide 1: WF on support of UL grant-free for NR
Huawei, HiSilicon, China Telecom, Fujitsu, InterDigital
3GPP TSG RAN WG1 #86 R1-16xxxx
Gothenburg, Sweden, Aug. 22-26, 2016
Agenda item: 8.1.2.2

## Slide 2: Background
Agreements:
Autonomous/grant-free/contention based UL non-orthogonal multiple access has the following characteristics
  A transmission from UE does not need the dynamic and explicit scheduling grant from eNB
  Multiple UEs can share the same time and frequency resources
For autonomous/grant-free/contention based UL non-orthogonal multiple access, the following should be studied
  Collision of time/frequency resources from different UEs, solutions potentially including
    E.g., code, sequence, interleaver pattern
  UL synchronization (DL synchronization assumed)
    Case 1: Timing offsets between UEs are within a cyclic prefix
    Case 2: Timing offsets between UEs can be greater than a cyclic prefix, FFS the exact model of timing offsets
  Requirement for power control
    Case 1: Perfect open-loop power control, i.e., equal average SNR between UEs for potentially link level calibration
    Case 2: Realistic open-loop power control with certain alpha and P0 values
    Case 3: Close-loop power control
  Receiver impact

## Slide 3: Observations
Grant-free transmission brings
  Overhead reduction Saving both UL and DL signaling such as grant, scheduling request, etc;
  Latency reduction Simplified process will save end-end time;
  Energy saving since the UE can remain in DRX longer and able to quickly transmit when data arrives.
With the above benefits, grant-free operations is especially suited for the scenarios with
  Infrequent small packets
  Low latency applications/services

## Slide 4: Proposals
NR should target to support UL grant-free at least for mMTC
Note: RAN1 use the terminology of “grant-free” in short for “autonomous/grant-free/contention based” transmission, referring to UE transmissions without dynamic and explicit scheduling grant from eNB