## Slide 1: WF on further considerations of UL grant-free for mMTC
Huawei, HiSilicon, CMCC, Fujitsu
3GPP TSG RAN WG1 #86 R1-16xxxx
Gothenburg, Sweden, Aug. 22-26, 2016
Agenda item: 8.1.2.2

## Slide 2: Background
Agreements:
Autonomous/grant-free/contention based UL non-orthogonal multiple access has the following characteristics
  A transmission from UE does not need the dynamic and explicit scheduling grant from eNB
  Multiple UEs can share the same time and frequency resources
For autonomous/grant-free/contention based UL non-orthogonal multiple access, the following should be studied
  Collision of time/frequency resources from different UEs, solutions potentially including
    E.g., code, sequence, interleaver pattern
  UL synchronization (DL synchronization assumed)
    Case 1: Timing offsets between UEs are within a cyclic prefix
    Case 2: Timing offsets between UEs can be greater than a cyclic prefix, FFS the exact model of timing offsets
  Requirement for power control
    Case 1: Perfect open-loop power control, i.e., equal average SNR between UEs for potentially link level calibration
    Case 2: Realistic open-loop power control with certain alpha and P0 values
    Case 3: Close-loop power control
  Receiver impact

## Slide 3: Proposals (1)
The resource for grant-free transmission should be pre-defined/pre-assigned and re-configurable, which include
  Time/frequency resource
  MA signatures, e.g. codebooks, sequences, interleaver patterns
  RS/preamble
The following resource allocation methods are considered for grant-free transmission
  Case 1: The resource used by a UE is pre-assigned by eNB. The assignment can be implicit or explicit.
  Case 2: A resource pool shared by a group of UEs is pre-defined and for each transmission, a UE autonomously selects the resource according to some pre-defined rule

## Slide 4: Proposals (2)
Further studies should consider the following:
  Handling of collisions of MA signatures and/or collision of RSs/preambles
  Retransmission and potential combining, e.g. HARQ
  Link adaptation including MCS assigning, codeword selection etc.
  Switching procedures between grant-free transmission and grant-based transmission including trigger and disable of grant-free transmissions.
  UL with timing offsets between UEs are within a cyclic prefix (Case 1)
  Realistic open-loop PC (Power control Case 2)
  Advanced receiver capabilities