## Slide 1: WF on CBR Measurement
Ericsson, …
3GPP TSG RAN WG1 Meeting #86 R1-168079
22nd – 26th August, 2016 Gothenburg, Sweden
Agenda item: 7.2.2.2.3

## Slide 2: Background
It is urgent to define the BSR measurement in order to contribute the ETSI harmonized standard for ITS

## Slide 3: Proposals
Sensing for CBR is only performed on system time/frequency resources used for data.
The sensing for determining CBR for LTE ITS is performed over a measuring interval of all V2V data subframes within the previous 100ms as follows:
  The data system resources are divided into subbands
    FFS the number of subbands, preferably aligned with supported PC5 scheduling granularity in frequency domain.
  Each probe consists of measuring the average signal power S over a single data subband over a single subframe.
  The probe is declared busy if S exceeds a pre-defined power threshold
    Where {P} is the set of probes, BW(p) is the bandwidth of probe p and B(p) is a binary variable indicating whether the probe p is detected as busy
  FFS whether each probe in the probes set {P} consists of:
    Only data resources
    Data or SA resources or both
    Data or SA resources or but not both
  FFS whether the probes set {P} includes only the union of mode-2 pools, the union of mode-1 and mode-2 pools or all V2V subframes.