## Slide 1: WF on pools for V2X
Ericsson, …
3GPP TSG RAN WG1 Meeting #86 R1-168082
22nd – 26th August, 2016 Gothenburg, Sweden
Agenda item: 7.2.2.3

## Slide 2: Background
In LTE-V2V, Rel-12 DFN definition is reused.
  Organization in periods of 10240 subframes.
V2V booking protocol based on periods of P
  P=100 in proposal from [85-09].
Problems in pool design:
  100 does not divide 10240
  Some subframes are not available for V2V transmission (SLSS, etc.)

## Slide 3: Proposals
V2X uses the following logical indexing based on V2X periods defined in the following way:
  Each V2X period consists of 100 consecutive subframes
    Subframes used for transmission of SLSS are excluded from V2X periods.
    Nreserved subframes are excluded from V2X periods (and reserved) to ensure that 100 divides the number of available subframes (i.e. 10240 – #N_SLSS_subframes – Nreserved).
  100-bit patterns may be further applied to every V2X period to define pools of resources (e.g., for V2P, mode 1, mode 2, etc.).
    In shared carriers, NW signaling is used to transmit the 100-bit pattern identifying the subframes available for V2X transmission.

## Slide 4: Illustration
Each V2X period includes 100 subframes
  120 subframes are excluded and used for SLSS (blue)
  20 subframes are excluded and reserved (red)
    100 divides 10240 – (120+20) = 10100
    101 V2X periods of 100 subframes each are defined
Booking based on logical indexing:
  E.g. Last subframe in first V2X period (DFN=99) books last subframe in second V2X period (DFN=199)
  E.g. First subframe (DFN=200) in third V2X period books first subframe in sixth V2X period (DFN=504)
DFN 0
DFN 1
DFN 99
DFN 100
…
DFN 199
DFN 200
…
DFN 255 (SLSS)
DFN 256 (SLSS)
…
DFN 257 (SLSS)
DFN 302
DFN 303
…
1st V2X period
2nd V2X period
DFN 402
DFN 403
…
DFN 502
DFN 504
…
…
4th V2X period
DFN 503 (Reserved)
DFN 512 (SLSS)
DFN 513 (SLSS)
DFN 514 (SLSS)
DFN 603
DFN 604
…
DFN 254
DFN 258
DFN 511
DFN 515
3rd V2X period
5th V2X period
6th V2X period