## Slide 1: WF on timing design for PUSCH in UpPTS
CMCC
R1-168097
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22–26, 2016
Agenda item 7.2.9

## Slide 2: Background
In RAN#71, a new Work Item on Uplink Capacity Enhancements for LTE was approved, aiming for enhancing the uplink capacity of LTE by means of introducing uplink 256QAM, and supporting PUSCH transmission in UpPTS
The objectives of the work of PUSCH in UpPTS that related to RAN1 include
  Specify mechanism for supporting PUSCH transmission in special subframe with DwPTS of 6 OFDM symbols, GP of 2 OFDM symbols.
  Backward compatibility with legacy UEs is maintained

## Slide 3: Proposals
The following three alternatives are identified for PUSCH transmission in UpPTS
  Alt1: In UpPTS, independent data block(s) is transmitted as a separate transmission resource
  Alt2: Symbols in UpPTS are bundled with the following UL subframe for transmission
  Alt3:Two consecutive UpPTS resources are bundled together, so as to form one transmission unit
At least support Alt1 for PUSCH transmission in UpPTS
FFS supporting of Alt2 and Alt3

## Slide 4: Proposals
For Alt1
  Support synchronized HARQ timing
  For TDD UL/DL configuration 1~5, specify the timing from UL grant to PUSCH according to the following table, when supporting PUSCH transmission in UpPTS, i.e.,
    The UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE, adjust the corresponding PUSCH transmission in subframe n+k, where the k is in the following table
TDD UL/DL Configuration | DL subframe index n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 6 | 6 |  |  | 4 | 6 | 6 |  |  | 4
2 |  | 5 |  | 4 |  |  | 5 |  | 4 | 
3 | 4 |  |  |  |  |  |  | 4 | 4 | 4
4 |  |  |  |  |  |  |  | 4 | 4 | 4
5 |  |  |  |  |  |  |  | 4 | 4 | 

## Slide 5: Proposals
For Alt1
  For TDD UL/DL configuration 0, reuse the UL index field in UL grant to schedule PUSCH in UpPTS. In addition to the interpretations of UL index in current specifications, including a new interpretation of the UL index based on one of the following two options
    Option1: When MSB=0 and LSB=0, UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE,
      adjust the corresponding PUSCH transmission in subframe n+6, when n= 0 or 5;
      adjust the corresponding PUSCH transmission in subframe n+5, when n= 1 or 6;
    Option2: When MSB=0 and LSB=0, UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE,
      adjust the corresponding PUSCH transmission in subframe n+5, when n= 1 or 6;

## Slide 6: Proposals
For Alt1
  For TDD UL/DL configuration 6, use the DAI field to indicate the schedule of PUSCH in UpPTS, and the interpretations of the DAI field is down selected within the following two options:
    Option1: Replace the DAI field by UL index, and the UL index can be interpreted as
      When MSB=1 and LSB=0: UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE, adjust the corresponding PUSCH transmission in subframe n+k, with the value of k as the same in existing spec for TDD config. 6.
      When MSB=0 and LSB=1: UE shall adjust the corresponding PUSCH transmission in subframe n+6
      When MSB=1 and LSB=1: UE shall adjust the corresponding PUSCH transmission in both subframes n+ k and n+6, with the value of k as the same in existing spec for TDD config. 6.
    Option2: Use a reserved combination of DAI (DAI=1) to indicate a PUSCH grant in UpPTS
MSB=1, LSB=0
MSB=0, LSB=1
MSB=1, LSB=1
DAI = 0
DAI = 1

## Slide 7: Proposals
For Alt1
  For TDD UL/DL configuration 0~6, FFS the following options to determine the timing from PUSCH in UpPTS to the corresponding retransmission
    Option1: Only support adaptive HARQ transmission, i.e., the retransmission of a PUSCH in UpPTS is scheduled by a UL grant with NDI not toggled
    Option2: Support both adaptive and non-adaptive HARQ transmission. For non-adaptive HARQ transmission, the PHICH is used, and the PHICH timing is designed based on one of the following principles
      Principle1: To keep the backward compatibility, the PHICH corresponding to PUSCH in UpPTS can only be added in DL subframes including legacy PHICH region
      Principle2: The PHICH corresponding to PUSCH in UpPTS can be added in DL subframes without PHICH region, the backward compatibility issue is solved by implementation of eNB