## Slide 1: WF on TBS scaling design for PUSCH in UpPTS
CMCC
R1-168099
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22–26, 2016
Agenda item 7.2.9

## Slide 2: Background
In RAN#71, a new Work Item on Uplink Capacity Enhancements for LTE was approved, aiming for enhancing the uplink capacity of LTE by means of introducing uplink 256QAM, and supporting PUSCH transmission in UpPTS
The objectives of the work of PUSCH in UpPTS that related to RAN1 include
  Specify mechanism for supporting PUSCH transmission in special subframe with DwPTS of 6 OFDM symbols, GP of 2 OFDM symbols.
  Backward compatibility with legacy UEs is maintained
For PUSCH in UpPTS, one transmission solution is to transmit a new data block independently.
  Considering that at most 6 SC-FDMA symbols for PUSCH transmission in UpPTS, TBS determination for the PUSCH in UpPTS needs to be modified

## Slide 3: Proposals
For TBS selection for independent PUSCH transmission in UpPTS, the TBS selection method for PDSCH in DwPTS is reused.
  Set the PRB scaling factor according to available number of symbols for PUSCH in UpPTS.
    The scaling factor can be down selected in between example 1 or 2 in the following table.
    Further down selection is not precluded
Available SC-FDMA symbols for PUSCH | 1 | 2 | 3 | 4 | 5 | 6
RE ratio | 1/12 | 1/6 | 1/4 | 1/3 | 5/12 | 1/2
Scaling factor example 1 | 1/8 |  | 2/8 |  | 4/8 | 
Scaling factor example 2 | 1/8 |  |  | 3/8 |  |