## Slide 1: WF on observations on NB-IoT positioning performance
Ericsson, ZTE
R1-168114
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-27, 2016
Agenda item 7.2.11.1

## Slide 2: Background
At RAN#72, a new work item for Narrowband IoT (NB-IoT) enhancement was proposed. One important objective is to extend Rel-13 design to support positioning to further increase the market impact.
  Support of UTDOA or OTDOA:
    Study accuracy, UE complexity, UE power consumption for both UTDOA and OTDOA using NB-IoT and provide recommendation to RAN#73 on which one solution to adopt [RAN1]
      3GPP network operators are invited to provide inputs to RAN1#86 on their positioning requirements. Companies are encouraged to include both methods in their evaluations.
    Based on the study make a choice (either uplink positioning or OTDOA) during RAN#73

## Slide 3: Observations
Significant performance difference, both for OTDOA and UTDOA are observed.
For UTDOA, the performance various between 45 meters and 380 meters at 67-percentile
  Only one source shows the UTDOA positioning accuracy can be less than 50 meters at 67-percentile.
For OTDOA, the performance various between 11 meters and 427 meters at 67-percentile
  Two sources show the OTDOA positioning accuracy can be less than 50 meters at 67-percentile without using enhancement techniques.
If enhancement techniques are assumed, for OTDOA, the performance various between 7 meters and 75 meters at 67-percentile
  Compare to Rel-13 NB-IoT UE, higher complexity and measurement accuracy are needed for the enhancement techniques

## Slide 4: Observations
Positioning accuracy varies from different companies due the following reasons:
  The accuracy depends on the anticipated deployment as well as the assigned resources for positioning
  Use of different channel models give different results on the positioning performance.
  Lack of common understanding what is the acceptable UE complexity for the REL-14 UE for positioning.

## Slide 5: Proposal
It is proposed that RAN1 agrees on unified simulation assumptions and UE measurement accuracies target before continues the evaluation of the OTDOA and UTDOA performance.