## Slide 1: WF on URLLC System Outage Evaluation
Intel
3GPP TSG RAN WG1 Meeting #86 R1-168129
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item - 8.1.7

## Slide 2: Proposal
FTP Model 1 with mean packet arrival rate λ and fixed packet size is used for URLLC evaluation
  Packet size is fixed to 64 bytes
System reliability (SR) is defined as the number of successful transactions (that satisfied link reliability and latency target) divided by the total number of generated packets for a given packet arrival rate
System outage is defined as SO = (1-SR)
URLLC capacity C(L, R, SR) is the offered cell load that meets link reliability R, packet latency L and system reliability targets

## Slide 3: Proposal
In case of multiplexing with eMBB
  In each cell, drop 10 eMBB UEs with full buffer traffic