## Slide 1: WF on turbo code selection
3GPP TSG RAN WG1 #86 meeting
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda item 8.1.4.1
LG Electronics, Ericsson, CATT, NEC, Orange, IMT
R1-168164

## Slide 2
In RAN1#85, the following flexibility issue had been agreed
  FEC complexity supporting the full range of info block lengths and code rates with reasonable (details FFS) granularity should be compared instead of single info block length with some code rate.
    Companies should provide details of the range of info block lengths and code rates for which their complexity evaluations are conducted
Based on our results, LTE turbo decoders can have better area and energy efficiencies than those of LDPC decoders with full flexibility.
Background

## Slide 3
LTE turbo code should be supported for NR for at least low throughput including eMBB, mMTC, and URLLC
  It can support flexibilities of information block sizes and code rates
  Turbo code enhancement can be considered
FFS: high throughput
Proposal