## Slide 1: WF on Frequency Selective Precoding for NR UL MIMO
Samsung, Intel, NTT DOCOMO, Huawei
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 8.1.5
R1-168173

## Slide 2: Background
Frequency non-selective UL precoding was introduced in Rel.10
  Suboptimal for following environments
    Large UL system BW
    Clustered UL resource allocation
    Etc.

## Slide 3: Proposal
Frequency selective UL precoding (at least for digital beamforming) should be studied in NR
  Study UL precoder signaling
    Example 1: Signaling of multiple PMIs (subband) via single or two-level DCIs
    Example 2: Signaling of multiple PMIs via Data channel
    Example 3: For TDD, precoder calculation at the UE based on DL RS
      For TDD and reciprocity calibrated UE, UE recommends candidates UL precoders to BS based on the DL RS measurement, BS determines the final precoder
  Study the use of UL frequency selective precoding for both dynamic beamforming and semi-dynamic beamforming
  Study UL subband size (i.e. UL precoding granularity) considering following aspects
    Implicit (defined by spec.) or explicit (by eNB/UE decision) signaling support
    Whether to Align with DL or not